Transport networks – 7-8. Practice 2023.

Traffic design of urban roads and intersections - Worksheet

Task: determine the future traffic of a planned bridge – connected roads and junction

- Traffic design of road sections

| section | traffic pcu/h | capacity (2 lanes) | number of lanes |
| --- | --- | --- | --- |
| 1 – X |  | 1500 |  |
| X – 2 |  | 1500 |  |
| X – 3 |  | 1500 |  |

- Traffic design of a signalised intersection (X)

Intersection movements pcu/h

| leg | 1 | 2 | 3 | sum |
| --- | --- | --- | --- | --- |
| 1 |  |  |  |  |
| 2 |  |  |  |  |
| 3 |  |  |  |  |
| sum |  |  |  |  |

Phase order of movements

Design of green times (Time period: P = 90 s)	Zmin = ( F * 2,0 ) / ( 3600 / P )

Intermediate time: I = 3 * 5 = 15 s		összes zöld idő: (P – I) 	90 – 15 = 75 s

|  | traffic pcu/h | green time s at least | green time s designed | capacity saturation |
| --- | --- | --- | --- | --- |
| phase 1 |  |  |  |  |
| phase 2 |  |  |  |  |
| phase 3 |  |  |  |  |

- Traffic design of a roundabout (X)

number of circular lanes

|  | traffic | capacity | lanes |
| --- | --- | --- | --- |
| circular track |  | 1200 |  |

entry capacities and capacity saturation

|  | circular traffic | entering traffic | entry capacity | capacity saturation |
| --- | --- | --- | --- | --- |
| leg 1 |  |  | 1148 |  |
| leg 2 |  |  | 1076 |  |
| leg 3 |  |  | 1259 |  |